## Slide 1
ARC Presentation

## Slide 2
What does ARC mean?
A luminous electrical discharge between two electrodes or other points.
arc
noun
What is an ARC flash?
An arc flash (also called a flashover), is the light and
heat produced as part of an arc fault, a type of electrical
explosion or discharge that results from a low-impedance
connection through air to ground or another voltage
phase in an electrical system.
An electric arc between two nails.

## Slide 3
What do the acronyms mean?
IEC
International Electrotechnical Commission - non-profit, non-governmental international standards organization that prepares and publishes International Standards for all electrical, electronic and related technologies.
ATPV
Arc Thermal Protective Value - refers to the maximum incident energy (in calories per centimetre squared) that protective equipment can be exposed to and prevent to onset of a second-degree burn. Ratings are based upon the total weight of the fabric.
EBT
Energy Breakopen Threshold - The incident energy on a material
that results in a 50% probability of breakopen. Breakopen is defined
as any open area at least 1.6 cm² (0.5 in.²).
HRC
Hazard Risk Categories -
PPE 1 – 4-8 cal/cm²
PPE 2 – 8-25 cal/cm²
PPE 3 – 25-40 cal/cm²
PPE 4 – >40 cal/cm²
kA
Kilo Amps – One thousand amperes.

## Slide 4
What is article 11B?
Category III PPE must undergo annual checking by a Notified Body, in accordance with Article 11 of the PPE Directive. Manufacturers have two options, 11A or 11B. The Article 11B procedure is suitable for manufacturers of Category III PPE with an approved quality-control system, such as ISO 9000 or similar systems.
What is EN 61482-1-1, ‘Open Arc’?
What is EN 61482-1-2, ‘Box Arc’?
'Open Arc' test method (ATPV test and garment test). This replaces IEC 61482-1:2002. The 'Open Arc' test method is the same as the original North American method for measuring the Arc Thermal Performance Value (ATPV), as used in ASTM F1959. Materials or assemblies are given an ATPV value, expressed in kilojoules per square metre (kJ/m2), which can be converted into the familiar cal/cm2.
The “box arc” test method is based on the European method described in ENV 50354, with a heat transfer measurement. Materials are classified as Class 1 (4kA) or Class 2 (7kA). During this test, a fabric sample is exposed to an electric Arc produced by a 4kA or 7kA short circuit. In the test, the Arc does not last any longer than 500ms. The amount of heat transmitted through the sample is measured during and after the test.
What is article 11A?
This involves the Notified Body obtaining a random sample of recently manufactured items of PPE which are then tested by methods used in the original EC type-examination to ensure continuing compliance.

## Slide 5
What is a Calorie?
A calorie is the energy required to raise one gram of water one degree Celsius at one atmosphere. The onset of second-degree burns may occur from 1.2 calories/cm2. One calorie/cm2 can be equal to holding your finger over the tip of a flame of a cigarette lighter for one second.
Why wear ARC protection?
PPE provides protection after an arc flash incident has occurred and should be viewed as the last line of protection. Reducing the frequency and severity of incidents should be the first option and this can be achieved through a complete arc flash hazard assessment and through the application of technology such as high-resistance grounding which has been proven to reduce the frequency and severity of incidents. However use of PPE can be the difference between a workers life or death.
Who wears ARC protection?
Utility Workers
Power generation Workers
Industrial Electrical Workers
Rail Workers
Anywhere there is a chance of an electric current creating an ARC

## Slide 6
Layering?
When you begin to start layering up ARC garments on top of each other the protection Factor of the
garments also increases.
+
+
=
CARC22 (5.9cal/cm2)
CARC1 (5.0cal/cm2)
CARC3 (12.6cal/cm2)
Combined total cal/cm2 rating
+
The insulating layers of air between each layer of ARC material.

## Slide 7
CARC22
Layering
+
CARC1
5.9cal
5.0cal
=
16.6cal
CARC22
+
CARC3
5.9cal
12.6cal
=
36.2cal
CARC24
+
CARC4
5.9cal
10.8cal
=
25.1cal
CARC24
+
CARC52
5.9cal
16cal
=
43.6cal

## Slide 8
CARC22
+
CARC51
5.9cal
6.2cal
=
18.2cal
CARC22
+
CARC56
5.9cal
12.8cal
=
22.1cal
CARC22
+
CARC1
5.9cal
5.0cal
+
CARC3
12.6cal
=
44.1cal
Layering

## Slide 9
Layering
CARC22
+
CARC1
5.9cal
5.0cal
+
CARC3
12.6cal
=
37.4cal
CARC24
5.9cal
+
CARC6
10.8cal
CARC22
+
5.9cal
+
=
52.5cal
CARC24
5.9cal
+
CARC6
10.8cal

## Slide 10
CARC22
+
5.9cal
+
=
???cal
CARC24
5.9cal
+
CARC53
16cal
CARC22
+
5.9cal
+
=
???cal
CARC24
5.9cal
+
CARC53
16cal
CARC51
6.2cal
CARC56
12.8cal

## Slide 11
Associated Items
CNS25WCC6AEA
SU378GKGVB
SK202211
SUS18KGNE
SU378GOBKL
SU378GKTFG

## Slide 12
Thermals
CARC22
CARC24
CARC28

## Slide 13
Polo Shirts
CARC1
CARC2
CARC12
CARC51

## Slide 14
Trousers
CARC4
CARC5
CARC5SY
CARC52

## Slide 15
Sweat Shirts
CARC3
CARC8SY
CARC56

## Slide 16
Coveralls
CARC6
CARC7
CARC7SY
CARC53

## Slide 17
Jackets
CARC920
CARC925
HV1344
HV1964
Click ARC Fleece
Click Arc Soft Shell
Click Arc Class 2 (7kA) Jackets, Trousers & Coveralls
Coming Soon

## Slide 18
This presentation’s intellectual property and design where applicable belongs to: BEESWIFT Ltd, Delta Point, Greets Green Road, West Bromwich, B70 9PL. UK.
For further information please visit www.Beeswift.co.uk
Or contact a sales representative at sales@Beeswift.com